## Slide 1: SmartEXEC Mine Ventilation On Demand System at the Xstrata Nickel Rim South Mine, Sudbury, Ontario; Implementation and Results to Date Authors: Hugo Dello Sbarba, Simsmart Technologies, Montreal QC, Canada Erik Bartsch Xstrata Nickel, Sudbury, Ontario, Canada Josh Lilley, Hatch, Sudbury, Ontario, Canada

## Slide 2
U/G ventilation provides fresh air to workers, dilutes diesel equipment gases/ particulate matters, and evacuates dust and noxious gases.
In Ontario U/G ventilation requirements determined by legislation (100cfm/hp)
Ventilation systems are typically set to meet the requirement at peak production and operating conditions.
During periods of reduced operations, this results in ‘waste’
Introduction

## Slide 3
Ventilation on Demand (VOD) is the adjustment of ventilation equipment settings according to vehicle and personnel current status and location
VOD reduces the ‘waste’ by matching the ventilation to what is actually required in various parts of the mine.
Introduction

## Slide 4
Auxiliary (secondary) ventilation control
  Start and stop of an auxiliary fan:
    on a fixed schedule
    as vehicles or personnel enters heading
  Adjustment of auxiliary fan Variable Frequency Drive (VFD)
    To meet the required vehicles airflow demand within a given zone or
    To maintain adequate level of gases or temperature.
  Adjustable of dampers for multi-openings duct network
    To meet vehicles’ airflow demand at a given position
    To maintain adequate level of gases or temperature
VOD Implementation

## Slide 5
Primary ventilation control
  Adjustment of regulator and/or booster fans settings
    To meet vehicles’ airflow demands within different primary ventilation zones
    To maintain adequate level of gases or temperature
  Optimization of regulators, booster fans and primary fans settings to minimize energy consumption of the system while satisfying all airflow demands within the primary zones.
VOD Implementation

## Slide 6
Exhaust fans
Backfill Plant
Admin -
Workshops
Intake fans
Vent Shaft & Hoist
Main shaft (3 Hoists)
Compressor House
Nickel Rim South (NRS)

## Slide 7
Remote control ventilation equipment
  Instrumentation (flow and gas sensors)
  Automated flow regulators
  Remote control of Starters and VFDS
Automation and Communication system
  Ventilation equipment ↔ PLC ↔ Ethernet
  Ventilation equipment ↔ Remote I/O ↔ Ethernet
  Ventilation equipment ↔ Leaky feeder remote I/O ↔ Leaky feeder ↔ Leaky feeder remote I/O concentrator
  Ventilation equipment ↔ PLC ↔ Leaky feeders remote I/Os ↔ Leaky feeder ↔ Leaky feeder remote I/O concentrator
Tagging and Tracking system
VOD execution software: SmartEXEC
VOD Requirements

## Slide 8
Optimize usage of fresh air supply while supporting level of activity required to achieve planned production rates.
    Non production zones.
    Machinery Diesel “off” during shift.
    Maintenance or holiday periods as non operating time
    Blast clearing times- evacuate blast gases optimally
    Reduce power consumption
    Reduce natural gas consumption
NRS VOD Objectives and
Economic Justification
Independent evaluations resulted in identified potential savings of between 34% and 48%

## Slide 9
Stage 1: Remote/Manual Ventilation Control
    Manual control and event scheduling: intelligent HMI for surface/remote control (fans on-off or VFD speed set point, controllable doors, regulators/dampers)
Stage 2: Flow or gas control mode
    Control based on the gas concentration from sensors as well as airflow sensors (PID control loop)
Stage 3: Dynamic VOD
    Flow control via ventilation demand calculation: as a function of personnel location and machinery location & operating status (zone in/out gates coverage to full tracking coverage)
    Optimization control: air flow distribution and surface fans energy
NRS VOD Implementation

## Slide 10
2008 Q4 | VOD Scoping study completed
2009 Q1 | VOD Vendor review & selection.
Q2 | First automated underground regulator and air-monitoring station installed.
Q3 | All surface fan automation complete
Q4 | First underground aux fan controls commissioned
2010 Q1 | Stage 1 Complete (Remote Manual control)
Q2 | Simsmart VOD software installed
Q4 | Stage 2 Complete (Scheduled event based control). Tracking System VOD integration complete. Real-time air demand calculated.
2011 Q1 | Perform first Stage 3 operation (Dynamic VOD : Mobile equipment air-flow control)
Q2 | Surface main Fan dynamic speed optimization implemented
Q3-4 | Increase utilization of stage 2 and prepare for stage 3 operation.
Project Timeline

## Slide 11
Main Shaft
Headframe
Air Flow
System Control
U/G Ventilation
System operated/monitored
from Surface OC
Main Shaft
1280L
1480L
1520L
1660L
1700L
Vent Shaft
Supply Fans
Exhaust Fans
570m3/s
Capacity (-6.5kPa)
12 m3/s Up-cast
540m3/s shaft capacity
(12m/s)
NRS Ventilation Flow

## Slide 12
Server
Starters
VFD
User
interfaces
Switch Ethernet on each level
PLCs
OPC communication
to PLCs
Surface Ethernet
switch
Dampers and regulators
Gas and flow
measurements
VMS
Surface and underground
Measurement and control
infrastructure
Underground Wifi access
Personnel RF ID
detection
Machinery RF ID
detection and
operating status
reporting
…
Wifi
Access
point
Wifi
Access
point
Wifi
Access
point
Dynamic tracking system server
Dynamic
Tracking
system
SQL db

## Slide 13
Communicate back to nearest Automation Control Centre (ACC)
Primarily controlled from surface but autonomous operation possible if communication is lost.
Accutron Flow
Transmitter
Carbon Monoxide
Sensor
Oxygen
Sensor
Nitrogen Dioxide
Sensor
Flextor Regulator
PLC Panel
Pressure
Transmitter
Actuators
Air Monitoring Stations at RADs

## Slide 14
‘Intelligent’ portable sub-stations designed for 3 fan sizes (100hp,50hp, 30hp)
Remote monitoring and Start/Stop capability.
‘Plug-in’ or permanently wired.
Controlled by local Automation Control Centre (ACC).
Can operate independently if communication with surface is lost.
Auxiliary Fans

## Slide 15
Using existing wireless infrastructure
No additional infrastructure (e.g. positioning beacons) required.
Real time locating service (RTLS) uses Received Signal Strength Indication (RSSI) to indicate position (see right)
Hardware or ‘soft’ tags
Tagging and Tracking System

## Slide 16
SmartEXEC HMI

## Slide 17
Control of 2 x 4000 hp and 3 x 550 hp surface fans
Control of 119 auxiliary fans
Control of 17 air flow regulators on Return Air Drifts
Air flow regulators control air as a function of the air demand on each related mine level
Air distribution optimization on 13 levels
Energy (speed) optimization for surface fans
Flow control per level
Events and schedule control for all fans and regulators
Link to mine wide tagging and tracking system
Implemented Ventilation Control

## Slide 18
Model Flow Control results
  Main surface fans speed reduction
  Change in regulator position
  Main surface fans speed increase
  Regulator position set back to its initial setting
Implemented Ventilation Control
Regulator FIC123 Nickel Rim South mine, Model flow (orange) vs. measured flow (purple)

## Slide 19
Control strategy
  Always maintain one of the regulator at minimal resistance (80% opening)
  Control the surface fans from the settings of the regulator at the minimal resistance
    Opening < 80% surface fans speed will decrease
    Opening > 80% surface fans speed will increase
Implemented Ventilation Control

## Slide 20
Chart: VOD Electricity Savings
| May 2011 | June 2011 | July 2011 | Aug 2011 | Sept 2011 | Oct 2011 | Nov 2011 | Dec 2011
Surface Fans | 326.5652 | 275.9493 | 303.1114 | 219.3909 | 279.1421 | 284.9545 | 342.8927 | 299.7022
U/G Fans | 311.0979 | 224.6207 | 255.0832 | 330.3987 | 296.1394 | 188.0497 | 354.2937 | 575.5562
638
Current annual projection: 10,140 MWh of annual savings.
Expected to exceed this as further aux fans included under VOD control
Energy Savings
VOD Power Shed: Scheduling
501
558
549
575
473
697
876
Total MWh

## Slide 21
Implementing a full mine-wide control strategy controlling 17 regulators and 5 main surface fans to achieve optimal main fans operating point
Performing VOD control (starting and stopping fans from vehicles’ presence) in several auxiliary zones
Having remote control of more than 120 auxiliary fans
Performing daily event schedule during shift change on the 120 auxiliary fans and the 5 surface fans
Minimizing blast clearing times by creating scheduled events
Achievements

## Slide 22
Acknowledgements
Xstrata nickel
Hatch
Questions?